## SIXTEENTH SCHEDULE

(Paragraph 37)

MINIMUM NAVIGATION PERFORMANCE SPECIFICATIONS – SPECIFIED AIRSPACE AND NAVIGATION PERFORMANCE CAPABILITY

1.	For the purpose of paragraph 37 of the Regulation, the following navigation performance capability is specified, that is to say, a capability to ensure that:

(a)	the standard deviation of lateral errors in the track of the aircraft is not more than 6.3 nautical miles;

(b)	the proportion of the flight time of the aircraft during which the actual track of the aircraft is 30 nautical miles or more off the track along which it has been given an air traffic control clearance to fly is less than 5.3 x 10-4; and

(c)	the proportion of the flight time of the aircraft during which the actual track of the aircraft is between 50 and 70 nautical miles off the track along which it has been given an air traffic control clearance to fly is less than 13 x 10-5.

- For the purposes of paragraph 37 of the Regulation, the following airspace is hereby prescribed as North Atlantic Minimum Navigation Performance Specification airspace, that is to say, the airspace from flight level 285 to flight level 420 within the area defined by rhumb lines joining successively the following points:

N3410.00 W01748.00 		N8200.00 E03000.00 		N4500.00 W05300.00

N3630.00 W01500.00 		North Pole 			N4336.00 W06000.00

N4200.00 W01500.00 		N8200.00 W06000.00	 	N4152.00 W06700.00

N4300.00 W01300.00 		N7800.00 W07500.00 		N3900.00 W06700.00

N4500.00 W01300.00	 	N7600.00 W07600.00 		N3835.00 W06853.00

N4500.00 W00800.00	 	N6500.00 W05745.00 		N3830.00 W06915.00

N5100.00 W00800.00 		N6500.00 W06000.00 		N3830.00 W06000.00

N5100.00 W01500.00 		N6400.00 W06300.00 		N2700.00 W06000.00

N5400.00 W01500.00 		N6100.00 W06300.00 		N2700.00 W02500.00

N5434.00 W01000.00	 	N5700.00 W05900.00 		N3000.00 W02500.00

N6100.00 W01000.00 		N5300.00 W05400.00 		N3000.00 W02000.00

N6100.00     00000.00 		N4900.00 W05100.00 		N3139.00 W01725.00

N8200.00     00000.00 		N4500.00 W05100.00

thence by that part of the arc of a circle radius 100 nautical miles centered on N3304.00 W01621.00 to N3410.00 W01748.00.